## Slide 1
Captain Pat BOONE – Version 1.1 - July 30, 2007
This presentation requires Microsoft Powerpoint 2003-XP
Introduction to the B737-NG Vertical Situation Display (VSD)
This presentation requires Microsoft® PowerPoint 2003® or XP®. Animation will be incorrect and part of the text will be unreadable when using an earlier version of PowerPoint. You can download and install the free MS PowerPoint 2003 Viewer® This free Viewer allows you to view all presentations created by PowerPoint 97 till 2003 without interference to another PowerPoint development program installed on your PC. The Viewer is supported by Windows 2000 SP3 – Windows XP – Windows ME – Windows 98 SE (requires computer restart) – Windows Server 2003 If you have another PowerPoint development program installed on your computer, this program will take precedence to the MS PowerPoint 2003 Viewer. Therefore, you must : 1- download this presentation to your computer 2- from the Start Menu under All Programs, open the Microsoft Office PowerPoint Viewer 2003 and open this presentation file.

## Slide 2: Introduction to the B737-NG Vertical Situation Display (VSD)
Altitudes
Waypoints
Climb / Descent
Terrain
Approach
Failure Flags
Slide <number>
This introduction to the VSD covers the following items :
The purpose of the VSD is to present a clear graphical picture of the airplane’s vertical flight path for enhancing the flight crews’ vertical situation awareness. The VSD depicts the vertical situation of the airplane relative to the terrain throughout all phases of flight. The VSD also depicts the vertical situation of the airplane relative to the runway during final approach. The VSD complements the increased use of constant-angle, area navigation and RNP approaches by providing immediate validation of the selected approach path and allowing full-time monitoring of the airplane position relative to the selected glide path.

## Slide 3
32000
24000
16000
ARVOL FL180B
VEKIN
18000
Altitudes
Introduction to the B737-NG Vertical Situation Display (VSD)

## Slide 4: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD display - Altitudes
 Altitudes
The Altitude Reference Scale is displayed on the left side.
The scale changes auto-matically when selecting another horizontal range.
For all settings up to
80 NM, the scale ratio is fixed, so that a 3 degree approach will always appear the same.
7000
8000
4000
0
0
10
20
The Horizontal Distance Scale is displayed at the bottom of the VSD. The range shown on the VSD is one half the range selected on the EFIS control panel.
The bottom of the Airplane symbol indicates the current airplane altitude with reference to the Altitude Reference Scale on the left.
(shown here is 4700 feet)
Altimeter info comes from ADIRU 1
MCP selected altitude
is indicated in magenta above the Altitude Ref. Scale and displayed by
a magenta dashed line.
The BARO Minimums Pointer displays the barometric minimums selected on the EFIS control panel.
(shown here is 1800 feet)
.
Slide <number>
When selecting RADIO, the green line disappears and only the green pointer remains, at the BARO altitude.
.
The Vertical Flight Path Vector indicates current flight path angle as a function of vertical speed and ground speed. The length of the white line is fixed
at one half of the horizontal range.

## Slide 5
32000
24000
16000
ARVOL FL180B
VEKIN
18000
Waypoints
Introduction to the B737-NG Vertical Situation Display (VSD)

## Slide 6: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD display - Waypoints
 Waypoints
32000
24000
16000
ARVOL FL180B
VEKIN
The active Waypoint ID is displayed in magenta, all other waypoints from the FMC LEGS Page within the selected range are displayed white.
FI25L 1410
Different Altitude Constraint Symbols are displayed according to restrictions programmed in the FMC LEGS Page.
18000
Slide <number>

## Slide 7: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD display - Waypoints
 Waypoints
GS 261 TAS 259
Only waypoints within the cyan dashed Enroute Swath lines are displayed on the VSD.
In this example DME04 is outside the enroute swath and therefore not displayed on the VSD.
Slide <number>
TUE
18:03 Z
1.0 NM
CI28
TUE
The enroute swath lines are inhibited on takeoff and in approach when the airplane is within 6 NM of the runway and less than 3000 ft above field elevation.
The enroute swath
is 1 NM on each side of the airplane actual track line.
During turns, the swath edge on the inside of the turn opens in the direction of the turn.
The swath angle increases with the bank angle.
DME04
The same goes for Terrain profiles.
(see further)
DME04 will now show on the VSD
TUE
CI28
DME04

## Slide 8
32000
24000
16000
ARVOL FL180B
VEKIN
18000
Climb / Descent
Introduction to the B737-NG Vertical Situation Display (VSD)

## Slide 9: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD display - Climb / Descent
 Climb / Descent
32000
24000
16000
0
ARVOL FL180B
VEKIN
18000
- 250
18000
10
20
The MCP selected Vertical Speed is displayed by a magenta dotted line. The line appears only when the V/S mode on the MCP is selected.
You can use this line the same way as the “green banana” to adjust the required rate of climb or rate of descent.
Slide <number>
- 500
- 1200
- 1600
Note :
The MCP selected vertical speed line may show on one pilot’s VSD and not on the other pilot’s display, if that F/D side has [G/S] captured.

## Slide 10
32000
24000
16000
ARVOL FL180B
VEKIN
18000
Terrain
Introduction to the B737-NG Vertical Situation Display (VSD)

## Slide 11: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD Display - Terrain
 Terrain
20000
16000
12000
37000
Slide <number>
0
80
160
The Terrain Profile line represents the highest terrain within the enroute swath.
Terrain behind the airplane is drawn equal to the terrain at the current position.
VSD terrain uses the same color coding that is used to depict EGPWS terrain on the lateral map :
• green: terrain 250-500 ft or more below the airplane
• amber: terrain from 250-500 ft below to 2000 ft
above the airplane
• red: terrain more than 2000 ft above the airplane
The VSD will always show terrain profile, regardless TERR has been pressed on the EFIS control panel.
This allows the pilot to select WXR on the ND and still have terrain profile on the VSD !

## Slide 12
32000
24000
16000
ARVOL FL180B
VEKIN
18000
Approach
Introduction to the B737-NG Vertical Situation Display (VSD)

## Slide 13: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD Display - Approach
 Approach
CF34
RW34 136
FI34 1280
8000
4000
0
0
6000
10
20
Slide <number>
The Range to Target Speed Dot (RTSD) indicates where the airplane will achieve the FMC or MCP target speed, both during acceleration and deceleration.
The dot is blanked when the actual speed is within 5 knots of the target speed.
In this example, the airplane will reach the target speed (270 knots) in 6 NM.
The solid dot is replaced with an unfilled dot if target speed will not be achieved within length of the vertical flight path vector line.

## Slide 14: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD Display - Approach
 Approach
RW25L 218
FI25L 1410
0
2.5
5
Slide <number>
2000
1000
0
2500
The magenta FMC Approach Glidepath Angle Line is displayed for approaches that include a designated approach angle.
The line extends 10 NM for situational awareness and is anchored to the missed approach waypoint, not the runway.
For approaches that do not have a designated FMC approach angle, a cyan dashed 3-Degree Reference Line is displayed.
Two Decision Gates are displayed, the first one (white) at 1000 ft, the second one (amber) at 500 ft above field elevation.
The gates indicate suggested points where the airplane should be path and speed stable on approach.
Decision gate(s) that are below the missed approach altitude are not displayed…
The BARO minimums pointer and line turn amber when airplane descends below the selected minimum altitude. Reset with the RST switch on the EFIS control panel.

## Slide 15
32000
24000
16000
ARVOL FL180B
VEKIN
18000
Failure Flags
Introduction to the B737-NG Vertical Situation Display (VSD)

## Slide 16: Introduction to the B737-NG Vertical Situation Display (VSD)
VSD Display - Failure Flags
 Failure Flags
MOD RTE
MAP / TERR RANGE DISAGREE
Slide <number>
FMC runway data is not available.
EGPWS terrain data is not available.
RWY DATA
VSD TERR
VSD
Annunciation is replaced with VSD TERR INHIBIT when GPWS control panel TERR INHIBIT switch is in the inhibit position.
MAP RANGE DISAGREE Indicates selected range on the EFIS control panel is different than the MAP display range.
TERR RANGE DISAGREE Indicates selected range on the EFIS control panel is different than the Terrain display range.
MAP/TERR RANGE DISAGREE Indicates selected range on the EFIS control panel is different than the MAP and Terrain display ranges.
Route Waypoints Modification Annunciation ;
FMC active route is being modified. Only the active waypoint is displayed.
VSD feature has failed, the VSD cannot be displayed.
VSD TERR INHIBIT

## Slide 17: Introduction to the B737-NG Vertical Situation Display (VSD)
Slide <number>
That’s all, folks
About : This presentation is not copyright protected. Training Captains may use this presentation and make changes for unlimited use within your airline. Pat BOONE is captain on Boeing 737-767 and author of B737MRG.net - the pilot guide for B737 non-normals.